How To Design a Rocket Stove

Sizing the combustion chamber to the pot size

| Pot size | Entrance to combustion chamber L cm | Cross sectional Area of entrance L2 =A cm2 | Inner Perimeter of combustion chamber Pinner cm | Outer circumference of combustion chamber (assuming 5 cm thick bricks) Couter | Gap a =A/ Pinner Distance between the pot and the inner perimeter of the combustion chamber cm | Gap b =A/ Couter Distance between the pot and the outer edge of the combustion chamber cm |
| --- | --- | --- | --- | --- | --- | --- |
| 1-15L | 11cm by 11cm or 12.5 cylindrical | 121 122 | 44 39.2 | 87.9* 87.9* | 2.75 3.1 | 1.37 1.37 |
| 15-50L | 15 by 15 | 225 | 60 | 78.5 | 3.75 | 2.86 |
| 50-100L | 16.5 by 16.5 | 272.25 | 66 | 83.2 | 4.12 | 3.27 |
| 110L | 18by 18 | 325 | 72 | 88 | 4.5 | 3.6 |
| 100-200L | 20 by 20 | 400 | 80 | 94.2 | 5 | 4.24 |
| 200+ | 22 by 22 | 484 | 88 | 100 | 5.5 | 4.8 |

(*This is based on a common size single pot rocket stove that has a 28cm diameter stove body. Obviously a stove body with a larger diameter would   require an even smaller Gapb

The numbers that are given for Gap A and Gap B are minimums. If flow problems exist with these dimensions then the gaps can be increased by 5 mm.

The thickness of the insulation under the pot is equal to the height of the pot supports minus the required Gap.

Take the 20cm by 20cm combustion chamber as an example.  If 6 cm pot supports are used and we require a 4.24 cm Gap B    then we need to fill under gap B  with 1.76 cm of insulation.  Notice that in the plans a 1.7 cm square mould is welded on the stove at Gap B

)

To calculate   Gap A  ( the distance between the pot and the inner perimeter of the combustion chamber) use the equation:

Gap A       = 	      Area

Inner Perimeter of combustion chamber

To calculate   Gap B   (between the pot and the outer edge of the combustion chamber) use:

Gap  B                  =          Area

Circumference   = [(L+7-10 cm] *3.14)

To calculate the GapC   (under the outer edge of the pot and the stove body) use

Gap C	         =              Area

Circumference Pot

To calculate Gap D    (between the sides of the pot and the stove body) use

Gap D         = Gap C   * 0.75

Determining the volume of a pot or of a stove body

Volume= A (Cross sectional Area of cylinder)  * (H) Height of cylinder

Area = (r2  *3.14)

To determine the circumference of the pot skirt

C= D  *3.14

C = D   [Pot diameter  + Gap D + gap D + 1t (thickness of metal)]  * 3.14

## To determine the height of the combustion chamber use

Height of stove entrance = X

Height of combustion chamber above stove entrance = 1.5X

Total Height of combustion chamber (TH) = X + 1.5X + 5cm (for thickness of insulation)

For example, the 60L institutional stove has these approximate dimensions

TO determine the height of the shelf above the bottom of the combustion chamber use

Shelf height (SH) = 0.3X

Common dimensions for a single pot Rocket stove